## Slide 1
It was set to 1257 kN, obtained by dividing the design yield resistance by a partial factor of 1.36, focusing on quick- response repair in an emergency situation.
A model based on a standard design example for civil structures.
Versatile and Quick-response Repair of Corroded I-shaped Girder Ends with Doubler Plates and High-strength Bolts
BACKGROUND
KEYWORDS
Analytical Study on the Repair Effect of Using Similar Doubler Plates
METHOD
RESULTS
SUMMARY
Osaka Metropolitan University Graduate School of Engineering Bridge Engineering Lab Taishi INOUE
Fig. 1 Corrosion Damage and Doubler Plate Repair
Corroded I-shaped girder ends have recently been repaired with double plates and high-strength bolts as a countermeasure against corrosion caused by water leakage and confined spaces. This repaired part should be versatile, that is, designed with strengthening and stiffening effects, resilience, workability, and cost-effectiveness in mind as corrosion distribution and extent are various.
Purpose
Girder End, Doubler Plate Repair, Repair Effect
DMG1
DMG2
DMG3
DMG4
100 mm
300 mm
Fig. 2 Analysis model
Table. 1 Recovery Assessment Results
Recovery Target
Proportional limit load shall exceed the target recovery load.
The vertical shortening of the cruciform column at the target recovery load shall not exceed that of the intact condition (0.9 mm).
The proposed repair method was confirmed to satisfy the recovery performance requirements under several corrosion conditions.
The proportional limit load was found to be lower than the yield resistance. Therefore, refining the definition of the effective resisting section in the design procedure could improve the rationality of the doubler plate design.
Fig. 3 Corrosion Case
Corrosion Area
Corrosion Case:
DMG1～4
Doubler Plates:
Combination: angle + plate
Repaired Area:
Equal to section loss of DMG1 cruciform column
D.Plate location:
Loss of end-side web → angle at girder end side
Otherwise → angle at span side
All cases satisfied the recovery target.
The recovery performance is evaluated in other corrosion conditions.
In all cases, proportional limit load was lower than the design yield resistance of the cruciform column.
Fig. 5 Load–Displacement Relationship
Fig. 6 Mises Stress Contour
(At Proportional Limit Load )
Unit : N/mm2
Unit : mm
Fig. 4 Doubler Plate Dimensions
Repair effect evaluation of kitted doubler plates under several corrosion pattern
Stress concentration occurs above the sole plate's end due to a contact force, whose degree of freedom is linked by the MPC beam constraint at the reference point. This phenomenon reduces the proportional limit load.